## Slide 1: Autonomous Navigation Workshop
Simona Doboli
Assistant Professor
Computer Science Department
Hosftra University
Email: Simona.Doboli@hofstra.edu
January 14th, 2006
Hauppage High School
SPBLI - FIRST
Mark McLeod
Programming Coach
Hauppauge Team 358
Northrop Grumman Corp.
Mark.McLeod@ngc.com

## Slide 2: Case Study: Vex
On-Board
Controls
Ultrasonic
Rangefinder
IR
Rangefinders
Line
Followers

## Slide 3: Keep Your Distance
Maintains a constant distance from an obstacle via ultrasonic & IR rangefinders
User sets distance via potentiometer
P – power to the motors proportional to the error in distance
Obstacle must be perpendicular to sensor to reflect echo
Polaroid 6500

## Slide 4: Closed-Loop Feedback Ultrasonic Algorithm (P)
Initialize
Send Trigger Pulse
Listen & time echo
Filter echo results
Timer / interrupt process
Echo
Interrupt
Compare requested distance to echo
Right Distance
?
Yes
No
Motor Stop
Motor=
distance error* KP
* In this example
KP=5
distance error=1 to 25

## Slide 5: How The Sensor Works Timer / Interrupt Process
Program requests a sonar pulse
Pulse is set out
Program is told pulse is sent
Program is told when echo returns
Calculate the time it took
Wait before requesting another
For Devantech SRF05 Rangefinder
SRF05 (1-150”) $25

## Slide 6
Presentation slides at:
www.cs.hofstra.edu/~sdoboli
or
Team358.org
Questions/Help please email us.
Simona.Doboli@hofstra.edu
Mark.McLeod@ngc.com