## Slide 1
Blue Alliance
Driver Stations
Red Alliance
Driver Stations
Software:
FMS Lite – controls the matches
(http://www2.usfirst.org/2009comp/FMS/FMSLight.Setup.msi)
MatchMaker – generates a match list
(http://www.idleloop.com/matchmaker/download.php)
Scoring xls(game dependent) – to keep track of seeding
FMS Lite IP: 10.0.0.100
Subnet: 255.0.0.0
Team DS IP: 10.xx.yy.5
Subnet: 255.0.0.0
User login: Driver
Robot IP: 10.xx.yy.1
Subnet: 255.0.0.0
SSID: event
Bridge mode
Notes:
Lacks sound effects
Manual scoring
Hardware:
(2) Ethernet switches-4 ports
(1) Wireless-N router- 3 ports
(1) Windows laptop
(3) power strips
(3) extension cords for power strips
(2) 50’ Cat-5e or better
(6) 10’ Cat5e
(1) 3’ Cat5e
50’
50’
10’
10’
Optional power
Optional power
Field router IP: 10.0.0.4
Subnet: 255.255.255.0
SSID: event
v2011